## Slide 1: Indoor exposures to outdoor air pollution 2013 ACSA/AIA Housing Research Lecture Series Monday October 7, 2013
Brent Stephens, Ph.D.
Civil, Architectural and Environmental Engineering
Illinois Institute of Technology
brent@iit.edu
Advancing energy, environmental, and
sustainability research within the built environment
www.built-envi.com
Twitter: @built_envi

## Slide 2: What do you think of when you hear “air pollution?”
http://latimesblogs.latimes.com/photos/uncategorized/2008/08/11/olympicsmog_3.jpg
Notes: Image Sources:
http://psoglin.typepad.com/.a/6a00d8341c52aa53ef00e553d230d58833-800wi
http://www.magazine.ucla.edu/exclusives/air-pollution_cholesterol2.jpg
http://deannaroy.com/wp-content/uploads/2011/09/austin-fire.jpg
http://thecityfix.com/files/2007/08/traffic.jpg
http://upload.wikimedia.org/wikipedia/commons/f/ff/Air_.pollution_1.jpg

## Slide 3: What do I think of when I hear “air pollution?”
Americans spend almost 90% of their time indoors
  ~75% at home or in an office
Klepeis et al., J Exp. Anal. Environ. Epidem. 2001, 11, 231-252

## Slide 4: Indoor vs. outdoor air pollution
Air pollution is both an indoor and an outdoor issue
Many indoor pollutant sources
Outdoor pollutants also infiltrate indoors
Much of our exposure to outdoor air pollution occurs indoors
Health effects of indoor exposures are difficult to assess
Time-consuming, invasive, and costly
Many connections are already made with outdoor pollutants
There remains a need to advance knowledge of indoor exposures
  Can improve connections to health effects
  Can inform how building design and operation impacts exposures

## Slide 5: Some outdoor airborne pollutants are regulated
National Ambient Air Quality Standards (NAAQS)
US EPA and the Clean Air Act (1970)
Set limits for 6 “criteria” pollutants
Pollutants Regulated Outdoors
Carbon monoxide (CO)
Lead (Pb)
Nitrogen dioxide (NO2)
Ozone (O3)
Particulate matter PM2.5 and PM10
Sulfur dioxide (SO2)

## Slide 6: Sources of particulate matter
http://science.howstuffworks.com/environmental/green-science/air-pollution-heart-health2.htm
http://photo-junction.blogspot.com/2010/05/air-pollution-photos.html

## Slide 7: Particulate matter: Up close
Casuccio et al., 2004 Fuel Process. Technol.; Ormstad, 2000 Toxicol.; Hinds, 1999 Aerosol Technol.
gases
viruses
Particle
Diameter
tobacco smoke
diesel smoke
fungal spores
pollen
dust
1 nm 10 nm 100 nm 1 µm 10 µm 100 µm
allergen
Nasal
Upper
Tract
Lower
Tract
Respiratory
Deposition

## Slide 8: Particle deposition in the respiratory system
Hinds, 1999 Ch. 11
 PM10
 PM2.5
 Ultrafine
Most particles of outdoor origin are smaller than 100 nm
Urban
Traffic
Urban
Background
Rural
Costabile et al., 2009
Atmos Chem Phys

## Slide 9: Outdoor PM and health effects
Pope et al., 2002 J Am Med Assoc
PM2.5 and pediatric ER visits
PM2.5 and mortality
Rate ratio = Adjusted Mortality-rate ratios
Fine particles = mean PM2.5 concentration for several years in the 1980s
Steubenville, OH
Harriman, TN
St. Louis, MO
Watertown, MA
Portage, WI
Topeka, KS
Mean PM2.5 concentration measured outdoors in six cities over several years in the 1980s
Dockery et al., 1993 New Engl J Med
Strickland et al., 2010 Am J Respir Crit Care Med
3-day average PM2.5data measured outdoors in Atlanta, GA from 1993 to 2004

## Slide 10: Health effects: Outdoor air pollution and mortality
Fann et al., 2012 Risk Analysis
An estimated 130,000 deaths in 2005 in the US were related to outdoor PM2.5

## Slide 11: Indoor proportion of outdoor particles
Outdoor particles infiltrate into and persist within buildings with varying efficiencies
Chen and Zhao, 2011
Atmos Environ
Exposure to outdoor PM often occurs indoors
Often at home
Meng et al., 2005 J Expo Anal Environ Epidem
Kearney et al., 2010 Atmos Environ
Wallace and Ott 2011 J Expo Sci Environ Epidem
MacNeill et al. 2012 Atmos Environ
Williams et al., 2003 Atmos Environ
Kearney et al., 2010 Atmos Environ

## Slide 12: Mechanisms that impact indoor exposures to outdoor PM
Removal by AER and deposition to (or reaction with) surfaces
Penetration from outdoors
Air exchange
Deposition
HVAC filter removal
Change in indoor concentration in time
Contribution from air exchange
with
outdoors
Removal by airflow through HVAC system
P
λ
β (or k)
Cin = indoor concentration (#/m3)
Cout = outdoor concentration (#/cm3)
P = penetration factor (-)
λ = air exchange rate (1/hr)
k = surface deposition rate (1/hr)
f = fractional HVAC runtime (-)
η = filter removal efficiency (-)
Q = HVAC airflow rate (m3/hr)
V = indoor air volume (m3)
Notes: Chapter 2 – Literature Review

## Slide 13: Mechanisms that impact indoor exposures to outdoor PM
Removal by AER and deposition to (or reaction with) surfaces
Penetration from outdoors
Change in indoor concentration in time
Contribution from air exchange
with
outdoors
Removal by airflow through HVAC system
P
λ
β (or k)
“Penetration Factor”
If P = 1:
The envelope offers no protection
If P = 0:
The envelope offers complete protection
Cin = indoor concentration (#/m3)
Cout = outdoor concentration (#/cm3)
P = penetration factor (-)
λ = air exchange rate (1/hr)
k = surface deposition rate (1/hr)
f = fractional HVAC runtime (-)
η = filter removal efficiency (-)
Q = HVAC airflow rate (m3/hr)
V = indoor air volume (m3)
Notes: Chapter 2 – Literature Review

## Slide 14: Mechanisms that impact indoor exposures to outdoor PM
Removal by AER and deposition to (or reaction with) surfaces
Filter removal
HVAC operation
Change in indoor concentration in time
Contribution from air exchange
with
outdoors
Removal by airflow through HVAC system
P
λ
β (or k)
“Filter efficiency”
If η = 1:
The filter offers complete protection (when the system operates)
If η = 0:
The filter offers no protection (ever)
Cin = indoor concentration (#/m3)
Cout = outdoor concentration (#/cm3)
P = penetration factor (-)
λ = air exchange rate (1/hr)
k = surface deposition rate (1/hr)
f = fractional HVAC runtime (-)
η = filter removal efficiency (-)
Q = HVAC airflow rate (m3/hr)
V = indoor air volume (m3)
Notes: Chapter 2 – Literature Review

## Slide 15: Importance of source and removal mechanisms
Building envelope penetration
  Only recently has varying particle infiltration been implicated in observed health disparities with outdoor PM
    Largely by varying AER, not penetration factor
HVAC removal
  Prevalence of air-conditioning has been shown to be a modifier in PM2.5 and PM10 mortality
    Little information on filter removal efficiency and HVAC system runtime
Janssen et al., 2002 Environ Health Persp; Franklin et al., 2007 J Expo Sci Environ Epidem;
Bell et al., 2009 Epidemiology
Hodas et al., 2012 J Expo Sci Environ Epidem; Chen et al., 2012 Epidemiology

## Slide 16: Goals of this work
Further explore the impacts of building envelopes and HVAC filters on indoor PM of outdoor origin
  Key parameters:
  Particle penetration factor, P
  Particle removal by HVAC filter, ηQ/V
  HVAC system runtime, f
Using measured data from recent studies on residential (and some small commercial) buildings
Can we also predict these impacts?

## Slide 17: Particle infiltration measurements

## Slide 18: Measuring particle infiltration
gases
viruses
Particle
Diameter
tobacco smoke
diesel smoke
fungal spores
pollen
dust
1 nm 10 nm 100 nm 1 µm 10 µm 100 µm
20 – 1000 nm
Particles can penetrate through cracks in building envelopes
  Theoretically a function of:
    Crack geometry
    Air speed through leaks
Are building details and particle penetration factors correlated?
  e.g., air leakage parameters or building age
  Need a better test method for measuring P quickly
Applied a particle penetration test method in 19 homes
Liu and Nazaroff, 2001 Atmos Environ
Stephens and Siegel, 2012 Indoor Air

## Slide 19: PM infiltration: Test homes
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Stephens and Siegel, Indoor Air 2012 22(6):501-512

## Slide 20: Test method | Particulate matter (20-1000 nm)
b
Use first portion of
data to solve for k:
Use estimate of k and
all of the data to
solve for P:
a
P
k
k
Parameter Estimation
Outdoor
Indoor
λ = 0.48±0.01 hr-1
k = 3.24±0.03 hr-1
P = 0.62±0.06
Particle concentration (#/cm3)
Stephens and Siegel, Indoor Air 2012 22(6):501-512
Notes: Emidblue and maroon, arial, medium large everywhere.
From Fialkoff’s house, 1001 Brass

## Slide 21: Particle infiltration results
Particle Penetration Factors (20 – 1000 nm)
Mean (± SD) = 0.47 ± 0.15 | Range = 0.17 ± 0.03 to 0.72 ± 0.08
Stephens and Siegel, Indoor Air 2012 22(6):501-512
Notes: Add plot of deposition rates
Exp(GSD) = 1.9 hr-1

## Slide 22: PM infiltration: What can we learn?
Blower doors
  Used to measure air-tightness in buildings worldwide
Source: Energy Conservatory Blower Door Manual

## Slide 23: Blower door tests
Source: ASTM E 779 and ASHRAE Standard 119
Airflow
(m3 s-1)
Leakage Coefficient
(m3 s-1 Pa-n)
I/O Pressure Difference
(Pa)
Leakage Exponent
(dimensionless)
Estimated Leakage Area (cm2)
Normalized Leakage, NL (dimensionless)
Air Changes per Hour @ 50 Pa (hr-1)
Notes: ASHRAE Standard 119; ASTM E…

## Slide 24: PM infiltration and air leakage
Particle penetration factors (P for 20-1000 nm particles)
  Significantly correlated with coefficient from blower door tests (C)
  Spearman’s ρ = 0.71 (p < 0.001)
Association is strong, but predictive ability is low
Stephens and Siegel, Indoor Air 2012 22(6):501-512
Notes: Rho = whatever it is….

## Slide 25: PM infiltration: Outdoor particle source and air leakage
Leakier homes had much higher outdoor particle source rates
Potential socioeconomic implications: low-income homes are leakier
Chan et al., 2005 Atmos Environ
Stephens and Siegel, Indoor Air 2012 22(6):501-512

## Slide 26: PM infiltration and age of homes
Outdoor Source Term, P×AER (hr-1)
Older homes also had much higher outdoor particle source rates
Stephens and Siegel, Indoor Air 2012 22(6):501-512
Penetration factor (-)

## Slide 27: Measurements of HVAC filtration

## Slide 28: HVAC filter performance
Stephens and Siegel, Aerosol Sci. Technol. 2012 46(5), 504-513
Stephens and Siegel, Indoor Air 2013
ASHRAE Standard 52.2  MERV
Filter efficiency for 0.3 to 10 µm particles
1-inch depth

## Slide 29: Indoor particle removal rates
Submicron particle loss with HVAC system operating 100%
n = 5
n = 9
n = 3
where f = 1
Lognormal Dist.
Geo Mean = 1.0 hr-1
GSD = 1.85
Min = 0.31 ± 0.01 hr-1
Max = 3.24 ± 0.04 hr-1
MERV <5: 0.92 ± 0.46 hr-1
MERV 6-8: 1.09 ± 0.60 hr-1
MERV 11+: 2.32 ± 1.03 hr-1
Split by filter type
Stephens and Siegel, Indoor Air 2012 22(6):501-512
Probability distribution
Indoor loss rate (1/hr)
Notes: Low merv n = 5
Mid merv n = 9
High merv n = 3

## Slide 30: HVAC system runtimes
HVAC systems in U.S. homes typically only operate in response to indoor-outdoor climate conditions
  f varies in time
Previously collected dataset (ASHRAE RP-1299)
  8 residential systems and 9 light-commercial systems
  Monitored 1 day per month for 1 year (cooling period only)
  3,100+ hours of cooling operation over 114 days
  Explored data for system runtimes
Stephens et al., 2011 Building and Environment
HVAC Removal =

## Slide 31: HVAC system runtimes in 17 buildings
Mean HVAC runtimes ranged 10.7% to 55.3%
  Median f ≈ 21%
  Increased with indoor-outdoor ΔT
    Also with lower thermostat settings
Stephens et al., 2011 Building and Environment
Median increase in hourly runtime per °C rise in
average indoor-outdoor temperature difference: ~6% per °C

## Slide 32: Variations in exposures
Across observed range of envelope penetration, filter efficiency, and runtimes

## Slide 33: Implications for submicron PM exposure
Penetration factors ranged 0.17 to 0.72
AER ranged 0.13 hr-1 to 0.95 hr-1
Outdoor particle source terms ranged 0.02 hr-1 to 0.62 hr-1
  Factor of ~30 difference from lowest to highest
  Higher in older, leakier homes
Indoor removal rates ranged 0.31 hr-1 to 3.24 hr-1
  Factor of ~10 difference from least efficient to most efficient filter
  Varied with rated filter efficiency (particularly for high-efficiency)
HVAC fractional operation ranged 10.7% to 55.3%
  Factor of ~5 difference
  Varied with thermostat settings, occupancy, and outdoor climate

## Slide 34: Implications for submicron PM exposure
Combined effects:
 | Lower bound | Upper bound
Penetration factor, P | 0.17 | 0.72
Air exchange rate, AER (1/hr) | 0.13 | 0.95
Outdoor source term, P×AER (1/hr) | 0.02 | 0.62
Indoor loss rate, k + ηQ/V (1/hr) | 3.24 | 0.31
Fractional HVAC operation, f | 55.3% | 10.7%
I/O submicron PM ratio (Finf) | 0.01 | 0.70
Factor of ~60 to ~70 difference in indoor proportion of outdoor particles between:
A new airtight home with a very good filter and high HVAC operation, and
A leaky old home with a poor filter and low HVAC operation
Some potential for predictive ability using:
  Age of home
  Building airtightness test results
  Knowledge of HVAC filter type
  I/O climate conditions

## Slide 35: A cautionary tale
In a net-zero energy capable home

## Slide 36: Impacts of high-efficiency HVAC systems
One of the test homes (Site 15) had a dedicated mechanical ventilation system
Outdoor air supply duct ran through an energy recovery ventilator and was installed directly into the HVAC return plenum
Previous results were only for natural infiltration, when the system was unplugged and capped
  Relying on envelope leakage alone for ventilation air
We repeated the test a second time with the ERV/OAS unit operating…

## Slide 37: Impacts of high-efficiency HVAC systems
This home was responsible for both the lowest and the highest envelope penetration factors!
  Depending on whether or not the ERV was operating
Problem: The ERV/OAS was ducted to directly downstream of the HVAC filter

## Slide 38: Implications for design and construction
Importance of performance testing
  Blower door tests at a minimum
  More advanced IAQ tests would be ideal
Attention to detail
  Envelope air sealing
  HVAC system design and construction
  HVAC filter choice
Stay informed
  Keep an eye on the researchers and publications mentioned herein
  Plenty of opportunities to advance research in housing energy and IAQ

## Slide 39: Acknowledgments
Jeffrey Siegel at the University of Texas at Austin / University of Toronto
All of our homeowners and occupants
Funding
  University of Texas at Austin Continuing Fellowship
  NSF IGERT Award DGE #0549428
  ASHRAE Grant-In-Aid
  Thrust 2000 Endowed Graduate Fellowship
Questions/Comments
email: brent@iit.edu
web: www.built-envi.com
Advancing energy, environmental, and
sustainability research within the built environment