## Slide 1: Welcome!
Patient Safety Fundamentals for HC Architects – Part 1
HC 101 Series
Tuesday, August 9, 2016
2:00 pm – 3:00 pm ET
1:00 pm – 2:00 pm CT
12:00 am – 1:00 pm MT
11:00 am – 12:00 pm PT
Moderator
Tom Clark
Clark/Kjos Architects
Presenter
John Kreidich
McCarthy Building Companies
Notes: MODERATOR:
Welcome to “Patient Safety Fundamentals for Health Care Architects” part of the AIA Academy of Architecture for Health HC 101 Series.
I’m Tom Clark, today’s moderator.

## Slide 2: Academy of Architecture for Health (AAH) On-line Professional Development
The Academy’s multi-channel on-line approach provides emerging professionals, journeymen, and master professionals with convenient and economical opportunities to develop their chosen area of interest.
The HC 101 Series sessions are tailored to provide budding healthcare design professionals with conceptual and practical primer-level knowledge.
Notes: MODERATOR:
The Academy has adopted a multi-channel approach to on-line continuing education to provide emerging professionals, journeymen, and master professionals with convenient and economical opportunities to develop their chosen area of interest.

## Slide 3
Compliance Statement
“AIA Knowledge” is a Registered Provider with The American Institute of Architects Continuing Education Systems (AIA/CES). Credit(s) earned on completion of this program will be reported to AIA/CES for AIA members. Certificates of Completion for both AIA members and non-AIA members are available upon request.
This program is registered with AIA/CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product.
Questions related to specific materials, methods, and services will be addressed at the conclusion of this presentation.
Notes: MODERATOR:
This session complies with all requirements of The American Institute of Architects Continuing Education Systems (seven seconds and click)

## Slide 4
Copyright Materials
This presentation is protected by US and International Copyright laws. Reproduction, distribution, display and use of the presentation without written permission of the speaker is prohibited.
©2016 The American Institute of Architects
Notes: MODERATOR:
This session is copyright protected (three seconds and click)

## Slide 5
Course Purpose & Objectives
To enable and enhance your ability to:
  Comprehend the relationship between the Life Safety Code and Authorities having Jurisdiction and CMS.
  Understand the reasoning behind defend-in-place versus evacuation response to fire in a hospital.
  Identify appropriate elements of fire and smoke containment in hospital design including fire barriers, smoke barriers and smoke partitions.
  Employ rated assemblies and engineering judgments in design of fire barriers, smoke barriers and smoke partitions.
Notes: MODERATOR:
Here are the purpose and objectives of the course (seven seconds and click)

## Slide 6
AIA/CES Reporting Details
In order to receive credit, each attendee must complete the webinar survey/report form at the conclusion of the presentation.
Follow the link provided:
in the Chat box at the conclusion of the live presentation;
in the follow-up email you (or the person who registered your site) will receive one hour after the webinar.
All attendees will be eligible to receive: 1 AIA LU/HSW (AIA continuing education)
Notes: MODERATOR:
To obtain AIA credit see the person who registered your site – who will be receiving directions by email. Each attendee must complete the survey/report individually to receive AIA/CES credit.
Once completed you will have access to an AIA Knowledge Community folder that will include your AIA/CES certificate, a PDF of this presentation, and a transcript of attendee questions with presenter response.

## Slide 7
To Post Questions or Comments:
Submit a question to the moderator via the chat box.
Content-related questions will be answered during the Q&A portion as time allows.
Tech support questions will be answered by AIA staff promptly.
Notes: MODERATOR:
Here is how to submit questions to the speaker

## Slide 8: Patient Safety in Acute Care Hospital Design
Presented by John Kreidich AIA, CHC, LEED AP B+C
Two areas of primary concern:
Life-Safety – assuring that occupants in the event of a fire are protected from smoke as well as fire – an exit stair is of no use to a bedridden patient.
Environmental Safety – assuring that occupants are not exposed to materials posing a threat to life or health.
Today we will focus on the first area of concern – Life Safety.
Notes: MODERATOR:
I am pleased to introduce today’s presenter, John Kreidich, Manager of Healthcare Services for McCarthy Building Companies. For nearly half of his forty-plus year career, John Kreidich managed planning, design, and construction of healthcare facilities, including four years as Assistant VP of medical facility operations. John is presently the go-to resource for all hospital-related safety, infection control, sustainable building, and material/equipment procurement matters at McCarthy Building Company’s Central Healthcare Unit.
Now to address the issue of Patient Safety in Acute Care Hospital Design I give you John Kreidich.
PRESENTER – SPEAKS TO SLIDE
Our learning objectives today relate to life-safety with a primary focus on fire-safety issues.

## Slide 9: The Life Safety Code and its relationship with Authorities having Jurisdiction and CMS
The Life Safety Code exists today primarily because devastating, catastrophic fires in the twentieth century focused national attention on the inadequacies of life safety features in buildings.
A fire at St. Anthony Hospital in Effingham, IL, in 1949, actually killed 74 people, both patients and staff.
www.rarenewspapers.com-
Notes: PRESENTER:
Origins of the Life-Safety Code go back to 1916, evolving into the Building Exits Code in 1927 – a strictly advisory document. It wasn’t until 1948 that the Building Exits Code was written to be adopted by jurisdictions as legally enforceable.

## Slide 10: The Life Safety Code is published as NFPA 101
Despite its title, the standard is not a legal code, is not published as an instrument of law, and has no statutory authority in its own right. However, it is deliberately crafted with language suitable for mandatory application to facilitate adoption into law by those empowered to do so.
Notes: PRESENTER:
A code must be adopted by a jurisdiction to have statutory authority.

## Slide 11: The Health Care Facilities Code is published as NFPA 99
This code is referenced regularly throughout NFPA 101. Its focus is more on the MEP and operational aspects of health care facilities.
From the perspective of design and programming it gives criteria for provisions to maintain operation during events such as earthquakes or hurricanes.
Notes: PRESENTER:
NFPA 99 goes beyond fire safety issues

## Slide 12: Authorities Having Jurisdiction (AHJ)
When some or all of the Code is adopted as regulations in a jurisdiction, it can be enforced by inspectors from local zoning boards, fire departments, building inspectors, fire marshals or other bodies and authorities having jurisdiction.
Authorities Having Jurisdiction (AHJ) are typically the federal, state, county and/or municipal building inspectors. Jurisdictions can overlap and may even disagree.
Notes: PRESENTER:
Those empowered to enforce a code adopted by a jurisdiction are Authorities Having Jurisdiction or AHJ’s

## Slide 13: Joint Commission on Accreditation of Hospitals
Hospital regulation as we know it began in 1918, when the American College of Surgeons began inspecting hospitals using a single-page document called The Minimum Standard for Hospitals.
In 1951, the American College of Physicians, the American Hospital Association, the American Medical Association, and the Canadian Medical Association joined forces to create the Joint Commission on Accreditation of Hospitals (now called the Joint Commission) as a way to provide voluntary inspection and accreditation of hospitals.
Notes: PRESENTER:
Four independent organizations with a common interest in patient safety created the “Joint Commission” in 1951

## Slide 14: Centers for Medicare & Medicaid Services (CMS)
In 1965, the federal government established the Centers for Medicare & Medicaid Services (CMS). Hospitals that were accredited by the Joint Commission were deemed to be in compliance with the Medicare Conditions of Participation & therefore qualified for Medicare and Medicaid reimbursement.
In the late 1960s, federal rulemaking implementing the use of the Life Safety Code was approved and finalized that as of 1/1/1970, facilities had to meet the provisions of the Life Safety Code 1967 edition in order to continue to satisfy Conditions of Participation (COP) to qualify for Medicare/Medicaid reimbursement.
Notes: PRESENTER:
The roles of NFPA and The Joint Commission had been in-place with state and local jurisdictions for well over a decade before the start of federal Medicare, Medicaid and CMS.

## Slide 15: Upcoming Break for Questions and Comments
What are your thoughts on the relationship of The Life Safety Code with Authorities having Jurisdiction and CMS?
www.agilecoach.ca, July 16, 2015
Notes: PRESENTER:
We are taking questions for a mid-session Q&A break. Please type questions and comments in the text dialog box on your screen.

## Slide 16: CMS Adopts 2012 Editions NFPA 101 & NFPA 99
The U.S. Centers for Medicare & Medicaid Services (CMS) now require health care facilities to migrate from using the 2000 edition of NFPA 101®, Life Safety Code® (LSC) to the 2012 edition; and mandate direct compliance with the 2012 edition of NFPA 99, Health Care Facilities Code, for the first time.
Healthcare facilities are expected to update and comply with NFPA 101 and NFPA 99, respectively by November 7, 2016.
Notes: PRESENTER:
Having failed to keep itself current with national code updates, CMS created many unnecessary compliance issues for hospital architecture. The recent adoption of the 2012 code occurred just in time to miss the 2016 edition.

## Slide 17: CMS Modifications to NFPA 101 & NFPA 99
CMS determined it knew more about patient protection than the national, industry-wide consensus-based committees that produce NFPA codes.
Consequently it made modifications to NFPA 101 and 99 that are summarized in the following slides.
Notes: PRESENTER:
Not willing to leave well enough alone, CMS made its own modifications to NFPA 101 and 99 – summarized in the following slides

## Slide 18: CMS Modifications to NFPA 101 & NFPA 99
Corridor doors and doors to rooms containing flammable or combustible materials must be provided with positive latching hardware. Roller latches are prohibited on such doors under the CMS rule.
In consideration of a recommendation by the state survey agency or accrediting organization, CMS may waive specific provisions of the Life Safety Code that would result in unreasonable hardships but only if the waiver will not adversely affect the health and safety of the patients.
Notes: PRESENTER

## Slide 19: CMS Modifications to NFPA 101 & NFPA 99
Hospitals may install alcohol-based hand rub dispensers in its facility if the dispensers are installed in a manner that adequately protects against inappropriate access. This requirement from CMS differs from the Life Safety Code, which doesn’t have any requirements against inappropriate access.
When a sprinkler system is shut down for more than 10 hours, hospitals must either evacuate the building or portion of the building affected by the system outage until the system is back in service or establish a fire watch until the system is back in service.
Notes: PRESENTER

## Slide 20: CMS Modifications to NFPA 101 & NFPA 99
Buildings must have an outside window or outside door in every sleeping room, and for any building constructed after 60 days past the publication date of the rule, the sill height must not exceed 36 inches above the floor. Windows in atrium walls are considered outside windows for the purposes of this requirement. The sill height requirement does not apply to newborn nurseries and rooms intended for occupancy for less than 24 hours. The sill height in special nursing care areas of new occupancies must not exceed 60 inches.
Notes: PRESENTER

## Slide 21: CMS Modifications to NFPA 101 & NFPA 99
For an ASHE monograph exploring the specific differences between the 2000 and 2012 editions of the Life Safety Code
Visit http://www.ashe.org/management_monographs/mg2013crowley.shtml.
For an ASHE webinar explaining CMS Adoption of the 2012 Edition of NFPA 99 and What It Means for Health Care Facilities - Thursday, September 15
Visit http://www.ashe.org/education/webinars/index.shtml to learn more or register for this event.
Notes: PRESENTER:
Here is where to learn more about CMS and its adoption of NFPA 101 and 99
No need to copy these links. You or the individual who registered your site will receive an email one hour after completion of this session giving a link to the webinar Survey/Report Form. The form needs be completed individually for an attendee to get AIA/CES credit. Once completed you will have access to an AIA Knowledge Community folder that will include your AIA/CES certificate, a PDF of this presentation, and a transcript of attendee questions with presenter response.

## Slide 22: Break for Questions and Comments
What are your thoughts on the relationship of The Life Safety Code with Authorities having Jurisdiction and CMS?
Notes: MODERATOR:
It’s time to check our Q&A in-box. If you have not already, please type questions and comments in the text dialog box on your screen. We can always get to your submission later in the session.
HOST TO READ SELECTED QUESTIONS / COMMENTS TO THE PRESENTER

## Slide 23: Hospital Fire Fighting Defend-in-place Strategy
Hospital patients are generally not capable of taking self-preserving action during a fire – many are literally unconscious. Given the limited number of staff available to move patients on short notice, hospitals need to minimize patient movement.
Notes: PRESENTER:
Hospitals rely on “defend-in-place” features, systems and tactics. Evacuation is a last resort when it is no longer possible to keep the patient safe in its room or move to another zone on the floor – protected from fire and smoke by rated barriers.

## Slide 24: Hospital Fire Fighting Defend-in-place Strategy
https://www.youtube.com/watch?v=dE7Isx5Jkqk&feature=youtu.be&t=63
National Fire Protection Association
Notes: PRESENTER:
It should now be clear why mass evacuation is not a viable option in a hospital.

## Slide 25
Notes: INTENTIONALLY BLANK (this stops the YouTube audio)

## Slide 26: Elements of Fire and Smoke Containment
Notes: PRESENTER:
There are three fundamental forms of fire and smoke containment that serve specific purposes. Starting with the Fire Barrier.

## Slide 27: Fire Barriers
Fire barriers can be used to separate occupancies, isolate hazardous areas, create a horizontal exit, enclose an exit or create a shaft. They have fire resistance ratings measured in hours, ranging from half an hour to three hours.
Notes: PRESENTER:
Buildings occupied by people taking longer to exit in a fire will have barriers with higher ratings.

## Slide 28: Intumescent Fire Barrier Systems
<- Intumescent reaction triggered by heat
Intumescent material commonly used as a fire barrier is ineffective at controlling smoke
Notes: PRESENTER:
Can you see why an intumescent fire barrier is ineffective at controlling smoke?

## Slide 29: Fire Barrier / Fire Wall
https://www.youtube.com/watch?v=i_BjOLknl3M
Marty Huie
http://www.buildingcode.info/
Notes: PRESENTER:
Here is a short video describing a fire barrier

## Slide 30
Notes: INTENTIONALLY BLANK (this stops the YouTube audio)

## Slide 31: Elements of Fire and Smoke Containment
Notes: PRESENTER:
Smoke barriers need to be fire-rated as well.

## Slide 32: Smoke Barrier / Smoke Zone
https://www.youtube.com/watch?v=gxAQ8g7sO_s
Marty Huie
http://www.buildingcode.info/
Notes: PRESENTER:
Here is a short video describing a smoke barrier

## Slide 33
Notes: INTENTIONALLY BLANK (this stops the YouTube audio)

## Slide 34: Smoke barriers
These barriers serve to restrict the movement of smoke protected by a fire resistance rating of at least one hour
Notes: PRESENTER:
Here is a cross-section of a Smoke Barrier

## Slide 35: Elements of Fire and Smoke Containment
Notes: PRESENTER:
Unlike a smoke barrier, a smoke partition need not be fire rated. It merely limits transfer of smoke

## Slide 36: Smoke partitions
Though not as substantial as smoke barriers, smoke partitions also are designed to limit the movement of smoke throughout a structure.
Examples of smoke partitions can include corridors, walls that enclose a sprinkler-protected hazardous area, or lay-in acoustical tile ceiling with ducted HVAC.
Notes: PRESENTER:
Here is a typical application of a Smoke Partition

## Slide 37: Upcoming Break for Questions and Comments on:
Defend-in-place vs. Evacuation
Elements of Fire and Smoke Containment
http://www.businessinsider.com , Courtesy of Scott Adams
Notes: PRESENTER:
We are nearing your last chance to submit questions and comments. Send in yours by way of the text dialog box on your screen.

## Slide 38: Q&A time
If you have questions for today’s presenters, please submit them to the moderator via the chat box.
Content-related questions will be answered during this Q&A portion as time allows.
Notes: PRESENTER:
Here is how to submit questions and comments

## Slide 39: Rated Assemblies
UL listed assemblies are assured of acceptance.
Source document:
UL FIRE RESISTANCE DIRECTORY
Notes: PRESENTER:
This is the “Bible” of fire and smoke containment detailing.

## Slide 40: Rated Assemblies – Example Documentation
Notes: PRESENTER:
An example of the information contained in the UL Directory.

## Slide 41: Rated Assemblies – Engineering Judgements
When field conditions differ from original design or unanticipated construction hindrances are encountered and the field conditions cannot be easily or cost effectively redesigned, design recommendations are typically made by manufacturer qualified technical personnel proposing alternative methods that ensure the firestop system is not compromised.
Notes: PRESENTER:
But the UL Directory doesn’t cover every eventuality – that’s when an Engineering Judgement is called for

## Slide 42: Rated Assemblies – Engineering Judgements
These are sometimes referred to as “Engineering Judgments or EJs”. Since these recommendations are not based upon identical designs as that which were fire tested, it is important that they be developed using sound engineering principles and good judgment.
Notes: PRESENTER:
While ultimately up to the authority having jurisdiction, these three are typically reliable sources of engineering judgements

## Slide 43: Last Chance for Questions and Comments on:
Defend-in-place vs. Evacuation
Elements of Fire and Smoke Containment
Fire Rated Assemblies
Any more on the Life Safety Code and CMS
Notes: MODERATOR:
It’s time to once again check our Q&A in-box. There is still time to type questions and comments in the text dialog box on your screen.
MODERATOR TO READ SELECTED QUESTIONS / COMMENTS TO THE PRESENTER
We will respond to all questions including those we might not have time to answer during the live session. You or the individual who registered your site will receive an email one hour after completion of this session giving a link to the webinar Survey/Report Form. The form needs be completed individually for an attendee to get AIA/CES credit. Once completed you will have access to an AIA Knowledge Community folder that will include your AIA/CES certificate, a PDF of this presentation, and a transcript of attendee questions with presenter response.

## Slide 44: Thank you for joining us today!
This concludes the AIA/CES Course #AAH1601. The webinar survey/report form URL is listed in the chat box and will be included in the follow-up email sent to you in the next hour. Earn 1 AIA LU/HSW.
Survey Link: http://bit.ly/2auhEpS.
All attendees must report credit individually by completing the webinar survey/report form within the next 3 business days. Credit will automatically appear on your transcript within 2 weeks. Tablet and smartphone users must copy down the above survey link.
Please direct any further questions to knowledgecommunities@aia.org.
Notes: MODERATOR:
Thank you for your interest and attention. Thank you to our presenter John Kreidich
You can copy the URL on this slide, or see the person who registered your site – who will receive an email with directions at the close of this session. You must take the survey individually to get credit.

## Slide 45: Join us at the AAH!
• Receive Academy Update newsletters
• Access to resources
  Knowledge Repository
  Webinars
  Award programs
  Scholarships, Fellowships
  Emerging professionals benefits
  National and regional conferences and events
  Social media, publications, blogs and Twitter
Notes: MODERATOR:
We would love to have you join The Academy – here are some of the benefits of membership . . .

## Slide 46: To join AAH or update your account go to:
Click here
www.aia.org/aah
Notes: MODERATOR:
Here is how to join or update your account . . .

## Slide 47: Join us for more upcoming webinars*
Visit www.aia.org/aah for more information and to register.
Date | Series | Topic
09/13 | Masters Studio Series | Increasing your HCAHPS Scores Through Design
10/11 | Masters Studio Series | Lighting for Improved Environment of Care
11/08 | Masters Studio Series | Dublin Hospital – Post-occupancy Evaluation 7 years later
12/13 | Case Study Series | 2015 AAH Design award winner and Case Study archive pilot: UCLA Surgery and Cancer Center
*Dates and topics are subject to change
Notes: MODERATOR:
Why not register now to attend the September 13th Masters Studio Series Session – “Increasing Your HCAHPS Scores Through Design”
Hope to see you then!