## Slide 1
National Institute of Building Sciences
Eunice Noell-Waggoner, LC, IES
Edward L. Soenke, FCSI, AIA, CCS, NCARB

## Slide 2
The Institute’s Mission:
“. . . to serve the nation and the public interest by supporting advances in building sciences and technology to improve the built environment.”

## Slide 3
The Institute’s Low Vision Design Committee (LVDC) was established in November 2011 to:
“Address the needs of all occupants of the built environment, including those with low vision, through improvements in designs and operational procedures for new and existing facilities to enhance the function, safety, and quality of life.
Identify existing knowledge and needs for further research to accomplish these objectives.”

## Slide 5
Seven Major Points of the Guidelines:
1. Need: The ADA and ABA are not adequate to serve the needs of the growing population with low vision
2. More than lighting: Emphasize the importance of other architectural elements

## Slide 6
3. Site: The site and transition from outside are as important as the interior design.
4. Lighting design method: The illuminance method is standard practice for today; other methods might be more applicable in the future.
5. Different forms of low vision: Reconciling the different needs of various forms of low vision for an optimal solution.

## Slide 7
6. Seniors: The senior population is disproportionately affected by low vision
  other causes of low vision including traumatic head injury
7. Design integration: Integrating low vision design into the overall design process is the goal
  Thermal and energy implications are not included
  The purpose is to concentrate on design for people with low vision
  Design that does not support it’s occupants is inherently wasteful

## Slide 8
Document Content:
General Design Principals
  How we see
  Lighting Design Methods
  General Considerations
Site and Landscape Design
  Approaches to sites and building location
Architecture, Lighting and Interior Design
  Space Layout, furniture, fixtures, wayfinding, finishes, lighting, fenestrations, signals and controls
References
Technical Appendices

## Slide 9
Next steps:
Presentation at AIA National Convention.
Approach national standards writing organizations about developing a low-vision standard.
Seek placement for the LVDC committee on the A117.1 development committee.
Seek funding and commitments to further develop the design guideline with graphics.

## Slide 10
What is low vision?
20/70 acuity or worse after correction (glasses or surgery)

## Slide 11
  Population aged >=80 years
    from 9.3 million in 2000 to 19.5 million in 2030
Notes: Population size may not be news to those at this convention.
What might be news is that most of these people will be considered low vision.

## Slide 12
Physiological & Psychological effects
  Perception of quality of life (Psychological)
    At the top of the list of public health fears for Americans is vision loss (21%)
      Americans say their biggest concern about low vision is losing their ability to live independently (75%)
American Foundation for the Blind

## Slide 13
Physiological & Psychological effects (cont)
    Impaired Concentration and Learning
    Pain Perception
    Decreased Productivity
    Depression
    Links to facility satisfaction, quality of life = care demands ($$$$$$$$)
American Foundation for the Blind

## Slide 14
The clinical problems as we age
  Natural age related issues
    Reduction in retinal photoreceptors (Rods)
    Lens hardens (Presbyopia)
    Lens yellows (Opacification)
    Pupil gets smaller (Pupillary Miosos)
    Floaters
    Dark adaptation slows (Delayed rhodopsin regeneration)

## Slide 15
  Disease
    Cataracts
    Glaucoma
    Retinal Detachment
    Age Related Macular Degeneration
    Diabetic Retinopathy
    Retinitis Pigmentosa

## Slide 16
What do all these have in common?
  Reduced amount of light entering eye
        More light is required to see in general
  Increased light scatter in eye
          Greater likelihood of glare (Direct & Reflected)
  Reduction of blue wavelengths of light
          Circadian rhythm is compromised

## Slide 17
Physical Hazards
  Trips and falls
Centers for Disease Control and Prevention
5 Leading Causes of Unintentional Injury Deaths, United States
2000 - 2007, All Races, Both Sexes Ages: 65-85
National Center for Health Statistics (CDC)

## Slide 18
  Building elements can make a dramatic impact on a persons ability to reach their destination.
  Exterior Building Challenges
    Walking Surface
    Level Changes
    Reflective surfaces
    Lighting transitions

## Slide 19: Exterior Walking Surface: Avoid confusing patterns

## Slide 20: The intensity of sunlight reflects off walking surfaces with light values
Value comparison of old & new concrete
Walking surfaces should be medium to dark in value

## Slide 21: Clearly define walkway obstructions
Pedestrians with low vision might not detect the planters.
Few people with low vision use long canes
Clearly marked obstruction.

## Slide 22: Define changes of levels
Steps lack definition
+ Water hazard
Strong contrast strip on each step.

## Slide 23: Define curbs, ramps & steps
Contrast needed @ ramps & curbs to alert for trip hazards
Avoid tapered steps or add a handrail at the location.

## Slide 24: Avoid Reflective & Transparent Vertical Surfaces
Vertical mirrors at entry way create optical illusions leading to accidents.
Transparent panels lack
definition and create hazards.

## Slide 25
Interior Building Challenges
  Space Planning
  Signage & Wayfinding
  Floor patterns / Finishes
  Transition zones
  Low value contrast
  Lighting

## Slide 26: Space Planning: Be Consistent!
  Intuitive Reception desk location.
  Consistent Bathroom locations
  Avoid Circular routes.

## Slide 27: Increase contrast
Signage:
Contrast between letters and ground
Contrast between sign and wall

## Slide 28
Use high contrast features and accents
Highlight destinations
Delineate boundaries
Wayfinding

## Slide 29: Floor Patterns and Finishes
Pattern conceals the edge of the steps
Reflective surfaces are difficult to decipher

## Slide 30: Reflected Glare on a Polished Surface
Disability Glare:
Distorts the pathway
Reflected glare from:
Windows
Skylights
Electric down lights

## Slide 31: Inadequate Emergency Egress Lighting: National Fire Protection Agency
Inadequate for those with low vision
Same for Corridors & Stairs (Stairs are more hazardous)
Current Regulations:
  Initial average of one footcandle, not less than one-tenth of a footcandle
  Minimum to maximum ratio not to exceed 40 to 1

## Slide 32: ASHRAE/IES 90.1 - 2013
Higher LPD’s provided for Visually Impaired:
Table 9.6.1 (Pages 95 – 99)
Space type: Typical Visually impaired
Dining/Activity Areas: .65 2.65
Corridors: .66 .92
Lobbies: .90 1.80
Restrooms: .98 1.21
Building Type Typical Visually Impaired
Living Room/Recreation: .73 2.41
Chapel 1.53 2.21

## Slide 33
Resources:
National Institute of Building Sciences Low Vision Design Committee: “Design Guidelines for the Visual Environment”
http://www.nibs.org/?page=lvdc
Stephanie Stubbs: sstubbs@nibs.org
Illuminating Engineering Society: “ANSI-IES RP-28-16: Lighting and the Visual Environment for Seniors and the Low Vision Population” http://www.ies.org/store/
2014 FGI Guidelines for Residential Health, Care, and Support Facilities

## Slide 34: Key Learning, Process Improvements and Take-Aways
Low vision population is exploding
Designers must understand what creates low vision and the physical, physiological & psychological results
Different forms of low vision may respond best to different design solutions
Low vision design needs to be integrated into the overall design process (interior & exterior)
Supportive environments consider lighting, architectural elements, finishes, & signage
Federal guidelines, as they currently exist, do not adequately accommodate people with low vision
Know your resources:
  NIBS: “Design Guidelines for the Visual Environment”
  ANSI/IES RP-28-16: “Lighting and the Visual Environment for Seniors & Low Vision”

## Slide 35
PROJECT A
Architect: RDG Planning/Design
Photo: Kun Ahang

## Slide 36
PROJECT B
Architect: RDG Planning/Design
Photo: Kun Ahang

## Slide 37
PROJECT C
Architect: RDG Planning/Design
Photo: Kun Ahang

## Slide 38
PROJECT D
Architect: RDG Planning/Design
Photo: Kun Ahang

## Slide 39
PROJECT E
Architect: RDG Planning/Design
Photo: Kun Ahang

## Slide 40
PROJECT F

## Slide 41
PROJECT G