## Slide 1
Bio-inspired Robotic Swarm Construction
Paul Kassabian P.E, C.Eng, P.Eng
Simpson Gumpertz & Heger
Working with:
Justin Werfel (Wyss Institute, Harvard University)
Nathan Melenbrink (Wyss/ICD-Stuttgart)

## Slide 3
United States Pavilion, Expo ‘67
Montreal, Quebec, Canada
Architect: Buckminster Fuller

## Slide 8
3D Printed Glass Tower: Neri Oxman MIT Mediated Matter
SGH

## Slide 10
Schwerpunkt: Ralph Helmick
SGH

## Slide 13
FINAL FULL-SCALE PRINT
SGH

## Slide 14
  Rapid structural analysis of 3d forms from others (architect, client, etc.)
  Rapid generation of 3d forms to use as inspiration for design.
1: QUICK AND DIRTY APRROACH
SGH

## Slide 15
  Optimize shape for fabrication…no shop drawings, directly printed from the model.
  Multiple unique forms can be reviewed as a batch process.
2: FINAL AND DETAILED
SGH

## Slide 23
Collective construction
Simple rules leading to complex behavior.
The result emerges from the system’s desire and environmental/structural conditions.
  e.g. birds flocking, bees swarming, fish schooling…
With no blueprints or central storage of information, this provides for adaptability and robustness.
Bottom-up not top-down….
Notes: We want something adaptive, which can react to environmental changes, and which requires little direct human input – little design.
We give a set of goals, the robots construct it, and the structure doesn’t fall. At no step during the construction process is the structure unstable, even with all of the robots climbing on it.

## Slide 24
TERMES Project: Justin Werfel
Notes: The TERMES project is one example. Replaceable robots adaptively constructing a structure larger than themselves.
But more generally, what has been researched is the idea of stigmergy - of using the environment to store information instead
No direct communication because it is inefficient at large scales
No central blue-print – no robots dedicated to a certain area of construction
So what we need to do is take advantage of the information in the environment – even the passive information which the robots don’t themselves store

## Slide 27
Choose algorithm carefully…
Desire to build up: robot knows gravity.
Rules:
  Take new tube up as much as possible.
  If joint is ok, move to top and place tube.
  If joint is not ok, move down until ok and “reinforce”.
  Repeat…

## Slide 29
Notes: Robots are independent, only have access to local information
No direct communication:
Coordinate only through environment: Sense forces within the truss to guide building
This approach is inspired by stigmergy: robots’ building activity is guided by forces in the truss, that building activity in turn affects those forces for subsequent measurements
Some related work uses vision or other inputs, the novelty of this approach is a focus on force sensing
This approach could be useful for disaster relief, or other scenarios where it’s difficult or dangerous for humans to build

## Slide 30
Unachored so counterbalancing prevents toppling…
…until fracture…
Notes: When robots pay attention to forces, they can forestall breaking in the structure they build
By paying attention to

## Slide 31: Hardware Development
Detweiler, Vona, Yoon, Yun, Rus,
Robotics & Automation 2007
Tavakoli, Zakerzadeh, Vossoughi, Bagheri,
Int. Journal of Industrial Robots
Notes: This prototype had some success with locomotion, but also highlighted the difficulties of wheeled locomotion on common, readily available, building materials.
Additional sensors would be needed to maintain consistent grip force across inconsistent material dimensions.
Furthermore, the power draw of such locomotion may be considerably greater than alternative methods, such as that of Tavakoli et al or Detweiler et al.

## Slide 32
vs.
Notes: In this work, we consider a team of robots that are capable of Building without blueprints or any pre-specified plan
Materials installed in sequence
There are bridge-builder games where time is frozen, allowing for a dedicated blueprinting phase,
But our scenario is more akin to World of Goo, where the
changing forces acting on the truss affect building activity in real-time

## Slide 33: Future Work
Swarm of robots that autonomously builds structures according to high-level instructions
Design of a construction kit, including sensing and mechanical attachment
Design of a new robot to work with these materials
Agent-based control algorithms
Notes: The long term goal of future work is to develop a swarm of robots that is capable of autonomously building structures according to high level instructions, where those structures are capable of cantilevers and spans
This includes the design Design of a construction kit, including sensing and mechanical attachment – which we’re already working on
As well as the design of a new robot to work with this construction kit
We’re also working on the agent-based control algorithms
Using RF instruction beacons to guide swarm activity for large-scale outdoor applications

## Slide 39
Bio-inspired Robotic Swarm Construction
Paul Kassabian P.E, C.Eng, P.Eng
Simpson Gumpertz & Heger
Working with:
Justin Werfel (Wyss Institute, Harvard University)
Nathan Melenbrink (Wyss/ICD-Stuttgart)